DROUGHT MONITORING TASK FORCE

Drought Status Report

May 19, 2008

Statewide precipitation for the previous water year (October 1, 2006 through September 30, 2007) was below normal (81% of normal).  Statewide precipitation for the period from October 1, 2006 through May 16, 2008 was below normal (82% of normal).  Statewide precipitation for the period from January 1, 2008 through May 16, 2008 is in the normal range (90% of normal) and precipitation is in the normal range for each of the drought monitoring regions for this period. Precipitation greater than 85% of normal is considered to be in the normal range.  The relatively wet period from February 1 until May 16 has had a significant effect on accumulated precipitation deficits across the Commonwealth.   The following drought evaluation regions are currently below normal for the period beginning October 1, 2006; Big Sandy (75%), New River (79%), Roanoke (79%), Upper James (83%), Northern Virginia (83%), Northern Piedmont (79%), and the Northern Coastal Plain (80%).  Cumulative precipitation deficits for the period beginning October 1, 2006 improved by multiple percentage points across the Commonwealth since the last report.  The Middle James, Shenandoah, Chowan, York-James, Southeast Virginia, and Eastern Shore drought evaluation areas currently are in the normal range of precipitation for this extended period.    Appendix A contains precipitation tables for periods dating to October 1, 2006.  The long-range monthly climatologic outlook calls for equal chances of below normal, normal and above normal precipitation and temperatures for the Commonwealth through June of 2008.  The long-range seasonal outlook calls for equal chances of below normal, normal and above normal precipitation and temperatures for the Commonwealth through August 2008.

The latest NOAA drought monitor indicates significant improvement in drought conditions throughout the Commonwealth and is included as Appendix B.  Appendix C contains information from the national drought monitor with only Virginia displayed.  Currently less than 8% of the Commonwealth is experiencing drought conditions   The NOAA seasonal drought outlook through August 2008 indicates that drought conditions are likely to improve.  The seasonal drought outlook is included as Appendix D.

Seven day average streamflows for May 18 are normal in the majority of the Commonwealth with a small area in the southern portion of the Blue Ridge physiographic province where streamflows are below normal (10th to 24th percentiles).  While drought monitoring ground water levels data is scarce, ground water levels are generally in the lower range of expected water levels in areas east of Route 95 and are generally lower than normal in the area west of Route 95. Fifteen dedicated drought monitoring wells are at levels indicative of normal ground water levels and four are at levels indicative of moderate hydrologic drought (10th to 24th percentiles).  Ground water levels in the vast majority of dedicated monitoring wells have shown increases in water levels in the last month indicating a period of ground water recharge.  Some of the apparent increases in ground water levels recorded in dedicated monitoring wells may be due to the increase of pressure due to near surface saturation by the heavy rainfall events during early May.  The actual benefit of these rainfall events to ground water will likely be demonstrated by actual ground wwater levels in these welss around the first of June. Levels of most large reservoirs have continued to rebound over the last month and are now full.

While the Virginia Department of Health has not reported any impacts to public water supplies that have compromised their ability to provide the needs of their customers’ 28systems remain on voluntary water conservation requirements and 3 systems remain on mandatory water conservation requirements.  Appendix E contains a table of waterworks that includes systems that have initiated water conservation requirements.

The Department of Forestry reports that the spring wildfire season has ended and that recent precipitation has significantly increased forest fuel moisture conditions.    Since January 1st, The VDOF responded to more than 995 wildfires which have burned more than 25,000 acres, as well as damaging or destroying 15 homes and 44 other structures. On a positive note, the VDOF has saved or protected 563 homes and 371 other structures during this same period. These numbers are all well above 5 and 10 year averages for the period.  The next real threat for significant wildfire development will return later this fall.

The Virginia Department of Game and Inland Fisheries reports that boat ramps are all open with the exception of those closed for renovation or repairs.  Spring trout stocking is progressing on schedule with the only impacts being fish that are smaller then average due to the previous year's drought that reduced hatchery flows and necessitated reducing feeding.  The spring turkey season closed on Saturday May 17, and there have been minimal issues with fire due to the wet conditions.  Reservoir and stream flows have benefited significantly from the recent rains.  The Department is shutting down its largest trout production for renovations, and above average rainfall would be very beneficial in maximizing production at the other facilities.  Reproductive success of many fish species improves during springs and summers with average to slightly above average flows.  So far, 2008 is shaping up to be a good year for fish reproduction.

While the intensity of drought impacts has decreased significantly during the last month, the lower than normal level of ground water is still cause for some concern regarding the potential for drought impacts to intensify as the growing season progresses.   The significantly wet period form April 1 until now will likely forestall the development of drought conditions until early July at the earliest. It is important to remember that localized drought impacts, particularly agricultural drought impacts, are a normal occurrence in an “average” Virginia summer.

Reports from the Climatology Office of the University of Virginia, the National Weather Service, the Virginia Department of Agriculture and Consumer Services, the Virginia Department of Environmental Quality, and the United States Geological Survey follow.

Report of the Climatology Office of the University of Virginia

The past thirty days have seen continued widespread rainfall associated with a number of frontal passages. As a result, precipitation totals for April were above (or much above) normal for all regions.  Precipitation for the first half of May has been more variable, but only the most southwestern portions of Virginia have been significantly below normal.  Taken together, April and May mark the first protracted period of statewide above-normal precipitation in over a year.

Although the longer-range outlooks (through August) give little useful guidance, the pattern of frequent frontal passages seems likely to continue for the very near future.  Nonetheless, at this time of year it is expected that the primary mechanism for rainfall will shift to more scattered thunderstorm activity.  Now that the growing season is well underway, normal rainfall amounts will soon fail to compensate for moisture loss from evaporation and plant uptake.

As the summer progresses, there is an increasing likelihood that tropical cyclone activity will bring precipitation to the Commonwealth.  Since this hurricane season is forecast to be more active than average, tropical systems (or their remnants) may be an important factor in summer water availability.

Report of the National Weather Service

The 6-10 day and 8-14 day outlooks both suggest a continuation of the abnormally wet/cool regime that we have experienced for the last few weeks. This suggests we could go into early June before we make the typical summer transition from widespread precipitation events to a more convective/showery regime. This delay will be a benefit from the standpoint of water resources as we may extend the period when we may potentially benefit from additional ground water storage prior to moving into a high evapo-transpiration time of year.

Virginia Department of Agriculture and Consumer Services

Status of Agricultural Drought

According to the USDA Crop Weather Report released on May 12, 2008, 90% of topsoil moisture was adequate. Most areas in the state continue to receive significant rain but the total rainfall year-to-date is still below normal. The western and southwestern parts of the state did not get the heavy rain received by the eastern portion of the state in April.

Impact on the Dairy Industry

Dairymen are busy harvesting small grains for silage and planting corn.  The budgets of dairymen continue to be strained by the high cost of grain, hay, fertilizer, diesel fuel and other inputs. The reserve supplies of feed have been used up on nearly all farms.  The outlook is improving for spring pastures and hay crop yields.

Impact on Crops

Pastures grass is growing with recent rains and warmer temperatures in Central VA.  In the southwestern portion of the state grass and small grain crops are below normal.  Recent rains have significantly relieved drought conditions for Virginia farmers. In fact, many areas reported that wet conditions caused planting delays for corn and tobacco. With the condition of the hay crop improving and producers making their first cutting of the year, it appears as if hay shortages will be reduced or even eliminated.  Prices for hay have been higher than normal due to past shortages.  Prices for all types of hay are higher than 2006 with increases of 7% to 140%.  Farmers are hoping that increased supplies of hay will lead to lower prices in the upcoming months.

Nursery/Horticulture:

Virginia's Nursery and Landscape Industry reports that the recent rains have helped to provide needed soil moisture and to replenish depleted irrigation ponds from last year's drought.  Unfortunately, last year's drought reduced normal plant growth and much nursery stock did not achieve its expected annual increase in diameter, which would have increased the plant's value to the nurseryman. Landscapers often held off filling orders when conditions were too dry for digging and planting, resulting in commercial nursery sales being reduced by 35-40%. Nurseries and landscapers are playing catch up this spring and sales are very good; however, if the current trend of extremely wet conditions continues it could cause an increase in fungal disease problems in last year's root damaged and already stressed plant material. If severe drought conditions return again during the 2008 growing season, it could be catastrophic to Virginia's nursery and landscape industries.

Impact on Streams and Wells

Recent rains temporarily swelled small streams, creeks and rivers, but water levels quickly returned to below normal indicating low ground water levels.  April brought good rainfall to Northwest and Central Virginia, but Southwest Virginia is still very dry. The few scattered showers in the Southwest have done little to improve the drought situation. In Central Virginia water levels are improved but not normal. For the first time since November, Northwestern Virginia surpassed normal average monthly rainfall for April and Shenandoah County cautioned its citizens to conserve well water since very little refill has occurred over the winter months.

Disaster Designations

Due to the extreme agricultural drought, 93 Virginia counties and 34 independent cities received a Secretarial disaster designation in 2007 as a primary natural disaster area.  York and Arlington counties and the independent cities of Alexandria, Bristol, Falls Church, Poquoson, and Norton were named contiguous disaster areas.

Waivers for Hauling of Emergency Supplies Extended

At the request of the Virginia Department of Agriculture and Consumer Services (VDACS), the Virginia Department of Emergency Management (VDEM) authorized motor carrier exemptions to hours worked, and the Virginia Departments of Transportation and Motor Vehicles granted temporary waivers of registration and license requirements along with normal weight and width restrictions for carriers transporting emergency supplies of hay or animal feed.  The exemptions, which became effective at 6 a.m. August 11, 2007, have been extended through 6 a.m., June 15, 2008.  The exemptions apply to the entire state since every Virginia locality has received either a primary or contiguous drought disaster designation from the United States Department of Agriculture.

Virginia Department of Environmental Quality

Condition of Major Reservoirs

All major reservoirs are full or nearly full. Lake Anna was actually one foot above full last week due to heavy rains. Kerr Reservoir is five feet above the guide curve. The Corps is attempting to lower the elevation of the lake without flooding low lying farmland and bottomland hardwood forests.  The other two large Corps of Engineers Lakes, Lake Philpott and Lake Moomaw are also full.  Smith Mountain Lake is full.  Striper releases have not caused Smith Mountain Lake to subside.  Two large water supply reservoirs for the Western Virginia Water Authority that serve the Roanoke area were formerly a cause for concern. Now Carvins Cove Reservoir is 95% full and Spring Hollow Reservoir is 85% full.

United States Geological Survey

Streamflow and Ground Water Levels

Streams across the State are still responding to rains received last week.  Most streamflow gages are recording normal to above normal flows based on May flow statistics.  Analysis of 7-, 14-, and 28-day running average statistics shows similar normal or above normal flows.  However, some streamflow gages in southwest Virginia (Tennessee, Big Sandy, Kanawha, and the headwaters of the Roanoke River Basins) are recording flows below normal.  Storm precipitation totals for the last week were lower in southwest Virginia than in the rest of the State.

While some of the precipitation may become recharge to the ground-water system, an increasing per cent of the total is intercepted for evaporation and transpiration.  The best indication of how much of the precipitation recharges the ground-water system will be shown in the recession of the streamflow hydrographs.  If the hydrographs drop rapidly to pre-rain flows, then there was very little recharge.  If the hydrograph recession slows at some value above the pre-rain flows, then some ground-water recharge occurred.  Usually around mid-May in Virginia, precipitation changes from frontal origin to a more scattered convective origin.  The result of this is heavy localized precipitation, with many areas remaining nearly dry for long periods.

Ground-water levels have shown improvement over the last month, but the data coverage is limited and results are mixed with most wells recording below normal to normal ranges in water levels.  Streamflow conditions are still the best indicator of ground-water conditions in areas where there is limited well data.

Streamflow conditions based on daily values for May 16 are presented in Appendix F. Area summaries of 7-day average streamflows from the USGS drought watch web page show similar flow conditions and are presented in Appendix G.  Current conditions are generally higher than depicted by seven day average stream flows as flows continue to increase due to the recent significant precipitation events.  Ground water levels based on conditions on May 16 are presented in Appendix H.

##### APPENDIX A

Precipitation departures by Drought Evaluation Region.

|  | PRELIMINARY PRECIPITATION SUMMARY |  | Prepared: |
| --- | --- | --- | --- |
|  |  |  |  |  | 05/18/08 |
|  | DROUGHT |  | May 1, 2008 | - May 16, 2008 |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 1.26 | 2.33 | -1.08 | 54% |
| 2 | New River | 1.29 | 2.04 | -0.75 | 63% |
| 3 | Roanoke | 2.51 | 2.10 | 0.42 | 120% |
| 4 | Upper James | 1.71 | 2.07 | -0.36 | 83% |
| 5 | Middle James | 3.40 | 2.05 | 1.35 | 166% |
| 6 | Shenandoah | 2.66 | 1.86 | 0.80 | 143% |
| 7 | Northern Virginia | 6.39 | 2.10 | 4.29 | 304% |
| 8 | Northern Piedmont | 3.97 | 2.04 | 1.93 | 194% |
| 9 | Chowan | 2.31 | 1.98 | 0.33 | 117% |
| 10 | Northern Coastal Plain | 4.47 | 2.01 | 2.46 | 222% |
| 11 | York-James | 2.39 | 2.07 | 0.32 | 116% |
| 12 | Southeast Virginia | 1.79 | 1.87 | -0.08 | 96% |
| 13 | Eastern Shore | 3.46 | 1.70 | 1.76 | 203% |
|  | Statewide | 2.77 | 2.06 | 0.71 | 134% |
|  | DROUGHT |  | Apr 1, 2008 | - May 16, 2008 |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 6.70 | 6.09 | 0.61 | 110% |
| 2 | New River | 6.45 | 5.59 | 0.86 | 115% |
| 3 | Roanoke | 7.43 | 5.90 | 1.54 | 126% |
| 4 | Upper James | 6.61 | 5.47 | 1.14 | 121% |
| 5 | Middle James | 8.52 | 5.39 | 3.12 | 158% |
| 6 | Shenandoah | 7.03 | 4.78 | 2.25 | 147% |
| 7 | Northern Virginia | 8.70 | 5.40 | 3.30 | 161% |
| 8 | Northern Piedmont | 7.97 | 5.33 | 2.64 | 150% |
| 9 | Chowan | 9.20 | 5.41 | 3.79 | 170% |
| 10 | Northern Coastal Plain | 6.77 | 5.10 | 1.67 | 133% |
| 11 | York-James | 10.43 | 5.37 | 5.06 | 194% |
| 12 | Southeast Virginia | 10.10 | 5.12 | 4.98 | 197% |
| 13 | Eastern Shore | 7.53 | 4.62 | 2.91 | 163% |
|  | Statewide | 7.73 | 5.48 | 2.25 | 141% |

|  | DROUGHT |  | Mar 1, 2008 | - May 16, 2008 |
| --- | --- | --- | --- | --- |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 10.50 | 10.34 | 0.16 | 102% |
| 2 | New River | 9.00 | 9.26 | -0.26 | 97% |
| 3 | Roanoke | 10.47 | 10.17 | 0.31 | 103% |
| 4 | Upper James | 9.09 | 9.26 | -0.17 | 98% |
| 5 | Middle James | 11.62 | 9.45 | 2.16 | 123% |
| 6 | Shenandoah | 9.55 | 7.98 | 1.57 | 120% |
| 7 | Northern Virginia | 11.43 | 9.06 | 2.37 | 126% |
| 8 | Northern Piedmont | 10.60 | 9.14 | 1.45 | 116% |
| 9 | Chowan | 12.93 | 9.78 | 3.15 | 132% |
| 10 | Northern Coastal Plain | 10.08 | 9.38 | 0.70 | 107% |
| 11 | York-James | 15.11 | 10.06 | 5.05 | 150% |
| 12 | Southeast Virginia | 13.23 | 9.32 | 3.91 | 142% |
| 13 | Eastern Shore | 9.66 | 8.93 | 0.73 | 108% |
|  | Statewide | 10.80 | 9.52 | 1.28 | 113% |
|  | DROUGHT |  | Feb 1, 2008 | - May 16, 2008 |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 12.98 | 13.92 | -0.94 | 93% |
| 2 | New River | 10.74 | 12.19 | -1.44 | 88% |
| 3 | Roanoke | 12.68 | 13.48 | -0.80 | 94% |
| 4 | Upper James | 10.98 | 12.11 | -1.13 | 91% |
| 5 | Middle James | 14.22 | 12.57 | 1.65 | 113% |
| 6 | Shenandoah | 11.49 | 10.39 | 1.10 | 111% |
| 7 | Northern Virginia | 14.09 | 11.73 | 2.36 | 120% |
| 8 | Northern Piedmont | 13.00 | 12.11 | 0.89 | 107% |
| 9 | Chowan | 15.70 | 12.95 | 2.75 | 121% |
| 10 | Northern Coastal Plain | 12.59 | 12.52 | 0.07 | 101% |
| 11 | York-James | 18.80 | 13.59 | 5.21 | 138% |
| 12 | Southeast Virginia | 16.85 | 12.82 | 4.03 | 131% |
| 13 | Eastern Shore | 12.85 | 12.12 | 0.72 | 106% |
|  | Statewide | 13.22 | 12.65 | 0.57 | 104% |

|  | DROUGHT |  | Jan 1, 2008 | - May 16, 2008 |
| --- | --- | --- | --- | --- |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 15.25 | 17.65 | -2.40 | 86% |
| 2 | New River | 11.98 | 15.40 | -3.41 | 78% |
| 3 | Roanoke | 13.57 | 17.40 | -3.82 | 78% |
| 4 | Upper James | 12.25 | 15.39 | -3.14 | 80% |
| 5 | Middle James | 15.19 | 16.23 | -1.04 | 94% |
| 6 | Shenandoah | 12.48 | 13.24 | -0.76 | 94% |
| 7 | Northern Virginia | 15.47 | 15.01 | 0.46 | 103% |
| 8 | Northern Piedmont | 15.89 | 15.63 | 0.26 | 102% |
| 9 | Chowan | 16.88 | 17.06 | -0.18 | 99% |
| 10 | Northern Coastal Plain | 13.81 | 16.27 | -2.47 | 85% |
| 11 | York-James | 20.21 | 17.73 | 2.48 | 114% |
| 12 | Southeast Virginia | 18.36 | 16.98 | 1.38 | 108% |
| 13 | Eastern Shore | 14.65 | 15.68 | -1.03 | 93% |
|  | Statewide | 14.59 | 16.29 | -1.70 | 90% |
|  | DROUGHT |  | Dec 1, 2007 | - May 16, 2008 |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 18.16 | 21.29 | -3.13 | 85% |
| 2 | New River | 14.43 | 18.11 | -3.67 | 80% |
| 3 | Roanoke | 16.79 | 20.65 | -3.85 | 81% |
| 4 | Upper James | 15.21 | 18.34 | -3.13 | 83% |
| 5 | Middle James | 17.87 | 19.40 | -1.53 | 92% |
| 6 | Shenandoah | 15.42 | 15.83 | -0.41 | 97% |
| 7 | Northern Virginia | 18.50 | 18.11 | 0.39 | 102% |
| 8 | Northern Piedmont | 18.79 | 18.91 | -0.12 | 99% |
| 9 | Chowan | 21.02 | 20.08 | 0.94 | 105% |
| 10 | Northern Coastal Plain | 16.55 | 19.55 | -3.00 | 85% |
| 11 | York-James | 24.32 | 21.12 | 3.20 | 115% |
| 12 | Southeast Virginia | 22.02 | 20.16 | 1.86 | 109% |
| 13 | Eastern Shore | 19.22 | 18.92 | 0.30 | 102% |
|  | Statewide | 17.66 | 19.41 | -1.75 | 91% |

|  | DROUGHT |  | Nov 1, 2007 | - May 16, 2008 |
| --- | --- | --- | --- | --- |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 19.86 | 24.57 | -4.71 | 81% |
| 2 | New River | 14.88 | 21.14 | -6.26 | 70% |
| 3 | Roanoke | 17.27 | 24.01 | -6.73 | 72% |
| 4 | Upper James | 15.62 | 21.70 | -6.08 | 72% |
| 5 | Middle James | 18.39 | 22.91 | -4.52 | 80% |
| 6 | Shenandoah | 16.53 | 18.88 | -2.35 | 88% |
| 7 | Northern Virginia | 20.08 | 21.52 | -1.44 | 93% |
| 8 | Northern Piedmont | 19.66 | 22.71 | -3.05 | 87% |
| 9 | Chowan | 21.47 | 23.19 | -1.72 | 93% |
| 10 | Northern Coastal Plain | 17.66 | 22.69 | -5.04 | 78% |
| 11 | York-James | 25.14 | 24.49 | 0.65 | 103% |
| 12 | Southeast Virginia | 22.58 | 23.23 | -0.64 | 97% |
| 13 | Eastern Shore | 20.06 | 21.86 | -1.80 | 92% |
|  | Statewide | 18.46 | 22.64 | -4.18 | 82% |
|  | DROUGHT |  | Oct 1, 2007 | - May 16, 2008 |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 21.82 | 27.45 | -5.63 | 79% |
| 2 | New River | 18.59 | 24.31 | -5.72 | 76% |
| 3 | Roanoke | 20.89 | 27.72 | -6.83 | 75% |
| 4 | Upper James | 17.99 | 24.95 | -6.96 | 72% |
| 5 | Middle James | 22.01 | 26.75 | -4.74 | 82% |
| 6 | Shenandoah | 18.74 | 22.07 | -3.33 | 85% |
| 7 | Northern Virginia | 23.33 | 25.00 | -1.67 | 93% |
| 8 | Northern Piedmont | 22.67 | 26.70 | -4.03 | 85% |
| 9 | Chowan | 24.57 | 26.77 | -2.20 | 92% |
| 10 | Northern Coastal Plain | 23.03 | 26.20 | -3.17 | 88% |
| 11 | York-James | 28.98 | 28.02 | 0.96 | 103% |
| 12 | Southeast Virginia | 27.85 | 26.89 | 0.97 | 104% |
| 13 | Eastern Shore | 23.43 | 25.07 | -1.65 | 93% |
|  | Statewide | 21.77 | 26.14 | -4.37 | 83% |

|  | DROUGHT |  | Sep 1, 2007 | - May 16, 2008 |
| --- | --- | --- | --- | --- |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 23.07 | 30.91 | -7.84 | 75% |
| 2 | New River | 20.23 | 27.72 | -7.49 | 73% |
| 3 | Roanoke | 22.97 | 31.95 | -8.98 | 72% |
| 4 | Upper James | 20.24 | 28.45 | -8.21 | 71% |
| 5 | Middle James | 22.82 | 30.88 | -8.06 | 74% |
| 6 | Shenandoah | 20.68 | 25.74 | -5.06 | 80% |
| 7 | Northern Virginia | 24.50 | 29.07 | -4.57 | 84% |
| 8 | Northern Piedmont | 23.66 | 30.98 | -7.32 | 76% |
| 9 | Chowan | 25.53 | 31.20 | -5.67 | 82% |
| 10 | Northern Coastal Plain | 24.28 | 30.29 | -6.02 | 80% |
| 11 | York-James | 30.88 | 32.92 | -2.04 | 94% |
| 12 | Southeast Virginia | 28.58 | 31.32 | -2.74 | 91% |
| 13 | Eastern Shore | 24.99 | 28.68 | -3.70 | 87% |
|  | Statewide | 23.19 | 30.14 | -6.95 | 77% |
|  | DROUGHT |  | Aug 1, 2007 | - May 16, 2008 |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 24.25 | 34.74 | -10.49 | 70% |
| 2 | New River | 21.42 | 31.03 | -9.60 | 69% |
| 3 | Roanoke | 23.80 | 35.67 | -11.87 | 67% |
| 4 | Upper James | 21.69 | 31.78 | -10.09 | 68% |
| 5 | Middle James | 25.54 | 34.70 | -9.16 | 74% |
| 6 | Shenandoah | 23.46 | 29.07 | -5.61 | 81% |
| 7 | Northern Virginia | 26.36 | 32.92 | -6.56 | 80% |
| 8 | Northern Piedmont | 26.04 | 34.80 | -8.76 | 75% |
| 9 | Chowan | 27.54 | 35.51 | -7.97 | 78% |
| 10 | Northern Coastal Plain | 25.72 | 34.15 | -8.43 | 75% |
| 11 | York-James | 33.21 | 37.79 | -4.58 | 88% |
| 12 | Southeast Virginia | 32.06 | 36.44 | -4.38 | 88% |
| 13 | Eastern Shore | 27.48 | 32.55 | -5.07 | 84% |
|  | Statewide | 25.06 | 33.97 | -8.91 | 74% |

|  | DROUGHT |  | Jul 1, 2007 | - May 16, 2008 |
| --- | --- | --- | --- | --- |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 28.75 | 39.22 | -10.48 | 73% |
| 2 | New River | 24.35 | 34.82 | -10.47 | 70% |
| 3 | Roanoke | 27.08 | 40.06 | -12.98 | 68% |
| 4 | Upper James | 24.03 | 35.82 | -11.79 | 67% |
| 5 | Middle James | 27.90 | 39.11 | -11.21 | 71% |
| 6 | Shenandoah | 25.45 | 32.83 | -7.38 | 78% |
| 7 | Northern Virginia | 28.82 | 36.69 | -7.87 | 79% |
| 8 | Northern Piedmont | 27.57 | 39.20 | -11.63 | 70% |
| 9 | Chowan | 30.60 | 40.02 | -9.42 | 76% |
| 10 | Northern Coastal Plain | 27.14 | 38.60 | -11.46 | 70% |
| 11 | York-James | 36.65 | 42.89 | -6.24 | 85% |
| 12 | Southeast Virginia | 35.37 | 41.51 | -6.14 | 85% |
| 13 | Eastern Shore | 29.57 | 36.55 | -6.98 | 81% |
|  | Statewide | 27.79 | 38.31 | -10.52 | 73% |
|  | DROUGHT |  | Jun 1, 2007 | - May 16, 2008 |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 31.49 | 43.36 | -11.87 | 73% |
| 2 | New River | 27.39 | 38.67 | -11.28 | 71% |
| 3 | Roanoke | 30.00 | 43.95 | -13.95 | 68% |
| 4 | Upper James | 27.78 | 39.53 | -11.75 | 70% |
| 5 | Middle James | 31.25 | 42.62 | -11.37 | 73% |
| 6 | Shenandoah | 28.73 | 36.54 | -7.81 | 79% |
| 7 | Northern Virginia | 30.76 | 40.55 | -9.79 | 76% |
| 8 | Northern Piedmont | 29.72 | 43.21 | -13.49 | 69% |
| 9 | Chowan | 32.81 | 43.67 | -10.86 | 75% |
| 10 | Northern Coastal Plain | 29.00 | 42.16 | -13.17 | 69% |
| 11 | York-James | 38.84 | 46.30 | -7.46 | 84% |
| 12 | Southeast Virginia | 38.59 | 45.12 | -6.53 | 86% |
| 13 | Eastern Shore | 34.83 | 39.53 | -4.71 | 88% |
|  | Statewide | 30.65 | 42.10 | -11.45 | 73% |

|  | DROUGHT |  | May 1, 2007 | - May 16, 2008 |
| --- | --- | --- | --- | --- |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 33.24 | 48.18 | -14.95 | 69% |
| 2 | New River | 29.17 | 42.88 | -13.71 | 68% |
| 3 | Roanoke | 31.97 | 48.28 | -16.31 | 66% |
| 4 | Upper James | 29.80 | 43.81 | -14.01 | 68% |
| 5 | Middle James | 33.71 | 46.86 | -13.15 | 72% |
| 6 | Shenandoah | 30.92 | 40.38 | -9.46 | 77% |
| 7 | Northern Virginia | 32.02 | 44.89 | -12.87 | 71% |
| 8 | Northern Piedmont | 31.81 | 47.43 | -15.62 | 67% |
| 9 | Chowan | 35.70 | 47.76 | -12.06 | 75% |
| 10 | Northern Coastal Plain | 30.24 | 46.32 | -16.08 | 65% |
| 11 | York-James | 40.39 | 50.57 | -10.18 | 80% |
| 12 | Southeast Virginia | 40.55 | 48.98 | -8.42 | 83% |
| 13 | Eastern Shore | 36.57 | 43.05 | -6.49 | 85% |
|  | Statewide | 32.68 | 46.36 | -13.68 | 70% |
|  | DROUGHT |  | Apr 1, 2007 | - May 16, 2008 |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 37.70 | 51.94 | -14.24 | 73% |
| 2 | New River | 32.29 | 46.43 | -14.14 | 70% |
| 3 | Roanoke | 35.18 | 52.08 | -16.89 | 68% |
| 4 | Upper James | 33.30 | 47.21 | -13.91 | 71% |
| 5 | Middle James | 36.95 | 50.20 | -13.26 | 74% |
| 6 | Shenandoah | 34.49 | 43.30 | -8.80 | 80% |
| 7 | Northern Virginia | 35.75 | 48.19 | -12.44 | 74% |
| 8 | Northern Piedmont | 34.91 | 50.72 | -15.82 | 69% |
| 9 | Chowan | 40.13 | 51.19 | -11.06 | 78% |
| 10 | Northern Coastal Plain | 33.95 | 49.41 | -15.46 | 69% |
| 11 | York-James | 44.43 | 53.87 | -9.44 | 82% |
| 12 | Southeast Virginia | 45.07 | 52.23 | -7.16 | 86% |
| 13 | Eastern Shore | 41.12 | 45.97 | -4.86 | 89% |
|  | Statewide | 36.32 | 49.78 | -13.46 | 73% |

|  | DROUGHT |  | Mar 1, 2007 | - May 16, 2008 |
| --- | --- | --- | --- | --- |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 40.84 | 56.19 | -15.35 | 73% |
| 2 | New River | 36.32 | 50.10 | -13.77 | 73% |
| 3 | Roanoke | 38.87 | 56.35 | -17.47 | 69% |
| 4 | Upper James | 36.94 | 51.00 | -14.06 | 72% |
| 5 | Middle James | 40.00 | 54.26 | -14.26 | 74% |
| 6 | Shenandoah | 37.37 | 46.50 | -9.13 | 80% |
| 7 | Northern Virginia | 38.91 | 51.85 | -12.94 | 75% |
| 8 | Northern Piedmont | 37.34 | 54.53 | -17.20 | 68% |
| 9 | Chowan | 42.70 | 55.56 | -12.86 | 77% |
| 10 | Northern Coastal Plain | 36.76 | 53.69 | -16.93 | 68% |
| 11 | York-James | 46.15 | 58.56 | -12.41 | 79% |
| 12 | Southeast Virginia | 47.01 | 56.43 | -9.42 | 83% |
| 13 | Eastern Shore | 42.90 | 50.28 | -7.39 | 85% |
|  | Statewide | 39.39 | 53.82 | -14.43 | 73% |
|  | DROUGHT |  | Feb 1, 2007 | - May 16, 2008 |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 42.24 | 59.77 | -17.53 | 71% |
| 2 | New River | 37.98 | 53.03 | -15.05 | 72% |
| 3 | Roanoke | 40.92 | 59.66 | -18.73 | 69% |
| 4 | Upper James | 39.39 | 53.85 | -14.46 | 73% |
| 5 | Middle James | 41.97 | 57.38 | -15.41 | 73% |
| 6 | Shenandoah | 39.43 | 48.91 | -9.48 | 81% |
| 7 | Northern Virginia | 41.75 | 54.52 | -12.77 | 77% |
| 8 | Northern Piedmont | 39.78 | 57.50 | -17.72 | 69% |
| 9 | Chowan | 44.87 | 58.73 | -13.86 | 76% |
| 10 | Northern Coastal Plain | 39.27 | 56.83 | -17.57 | 69% |
| 11 | York-James | 47.90 | 62.09 | -14.19 | 77% |
| 12 | Southeast Virginia | 49.28 | 59.93 | -10.65 | 82% |
| 13 | Eastern Shore | 45.68 | 53.47 | -7.79 | 85% |
|  | Statewide | 41.48 | 56.95 | -15.47 | 73% |

|  | DROUGHT |  | Jan 1, 2007 | - May 16, 2008 |
| --- | --- | --- | --- | --- |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 45.42 | 63.50 | -18.08 | 72% |
| 2 | New River | 40.94 | 56.24 | -15.30 | 73% |
| 3 | Roanoke | 44.80 | 63.58 | -18.77 | 70% |
| 4 | Upper James | 42.40 | 57.13 | -14.73 | 74% |
| 5 | Middle James | 45.54 | 61.04 | -15.50 | 75% |
| 6 | Shenandoah | 40.99 | 51.76 | -10.77 | 79% |
| 7 | Northern Virginia | 43.99 | 57.80 | -13.81 | 76% |
| 8 | Northern Piedmont | 42.30 | 61.02 | -18.73 | 69% |
| 9 | Chowan | 47.39 | 62.84 | -15.45 | 75% |
| 10 | Northern Coastal Plain | 43.51 | 60.58 | -17.08 | 72% |
| 11 | York-James | 50.51 | 66.23 | -15.72 | 76% |
| 12 | Southeast Virginia | 52.45 | 64.09 | -11.64 | 82% |
| 13 | Eastern Shore | 47.85 | 57.03 | -9.18 | 84% |
|  | Statewide | 44.54 | 60.59 | -16.05 | 74% |
|  | DROUGHT |  | Dec 1, 2006 | - May 16, 2008 |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 47.41 | 67.14 | -19.73 | 71% |
| 2 | New River | 42.72 | 58.95 | -16.23 | 72% |
| 3 | Roanoke | 46.98 | 66.83 | -19.85 | 70% |
| 4 | Upper James | 44.39 | 60.08 | -15.69 | 74% |
| 5 | Middle James | 47.13 | 64.21 | -17.08 | 73% |
| 6 | Shenandoah | 42.11 | 54.35 | -12.24 | 77% |
| 7 | Northern Virginia | 45.65 | 60.90 | -15.25 | 75% |
| 8 | Northern Piedmont | 44.05 | 64.30 | -20.25 | 69% |
| 9 | Chowan | 49.56 | 65.86 | -16.30 | 75% |
| 10 | Northern Coastal Plain | 45.21 | 63.86 | -18.65 | 71% |
| 11 | York-James | 52.33 | 69.62 | -17.29 | 75% |
| 12 | Southeast Virginia | 54.90 | 67.27 | -12.37 | 82% |
| 13 | Eastern Shore | 50.60 | 60.27 | -9.67 | 84% |
|  | Statewide | 46.39 | 63.71 | -17.32 | 73% |

|  | DROUGHT |  | Nov 1, 2006 | - May 16, 2008 |
| --- | --- | --- | --- | --- |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 50.17 | 70.42 | -20.25 | 71% |
| 2 | New River | 46.67 | 61.98 | -15.30 | 75% |
| 3 | Roanoke | 52.37 | 70.19 | -17.81 | 75% |
| 4 | Upper James | 48.17 | 63.44 | -15.27 | 76% |
| 5 | Middle James | 52.86 | 67.72 | -14.86 | 78% |
| 6 | Shenandoah | 46.26 | 57.40 | -11.14 | 81% |
| 7 | Northern Virginia | 51.45 | 64.31 | -12.86 | 80% |
| 8 | Northern Piedmont | 50.35 | 68.10 | -17.75 | 74% |
| 9 | Chowan | 56.93 | 68.97 | -12.04 | 83% |
| 10 | Northern Coastal Plain | 50.51 | 67.00 | -16.49 | 75% |
| 11 | York-James | 57.99 | 72.99 | -14.99 | 79% |
| 12 | Southeast Virginia | 62.52 | 70.34 | -7.82 | 89% |
| 13 | Eastern Shore | 55.48 | 63.21 | -7.73 | 88% |
|  | Statewide | 51.55 | 66.94 | -15.39 | 77% |
|  | DROUGHT |  | Oct 1, 2006 | - May 16, 2008 |
|  | REGION | OBSERVED | NORMAL | DEPARTURE | % OF NORM. |
| 1 | Big Sandy | 55.14 | 73.30 | -18.16 | 75% |
| 2 | New River | 51.66 | 65.15 | -13.49 | 79% |
| 3 | Roanoke | 58.41 | 73.90 | -15.48 | 79% |
| 4 | Upper James | 55.10 | 66.69 | -11.59 | 83% |
| 5 | Middle James | 60.56 | 71.56 | -11.01 | 85% |
| 6 | Shenandoah | 51.50 | 60.59 | -9.09 | 85% |
| 7 | Northern Virginia | 56.23 | 67.79 | -11.56 | 83% |
| 8 | Northern Piedmont | 56.88 | 72.09 | -15.21 | 79% |
| 9 | Chowan | 64.63 | 72.55 | -7.92 | 89% |
| 10 | Northern Coastal Plain | 56.59 | 70.51 | -13.93 | 80% |
| 11 | York-James | 65.99 | 76.52 | -10.53 | 86% |
| 12 | Southeast Virginia | 67.58 | 74.00 | -6.41 | 91% |
| 13 | Eastern Shore | 62.41 | 66.42 | -4.01 | 94% |
|  | Statewide | 57.79 | 70.44 | -12.65 | 82% |

##### APPENDIX B

APPENDIX C

APPENDIX D

APPENDIX E

Condition of Public Water Supplies

April 18, 2008

| ODW Drought Situation Report |  |  | Restriction totals |  |  |
| --- | --- | --- | --- | --- | --- |
| Date: | 5/14/08 |  | Mandatory | 3 |  |  |
|  |  |  | Voluntary | 28 |  |  |
|  |  |  | Total | 31 |  |  |
|  |  |  | N-None | B-Better |  |  |
|  |  |  | M-Mandatory | S-Stable/Same |  |  |
|  |  |  | V-Voluntary | W-Worse |  |  |
| PWSID | Waterworks | Source Name | Restrictions | Situation | Population Served |  |
| 1105400 | Lee County PSA | KVS Quarry | N | S 05/12/08: Water level in quarry is holding steady compared to last month; level falls about an inch and then rises about an inch with rainfall; currently at 133.5 inches below catwalk . Level was 132 inches below catwalk on 04/14/08. | 2,500 |  |
| 1169725 | Town of Nickelsville | Wells | N | B 05/13/08: Well production had dropped and voluntary conservation notice issued 8/31/07. Well production steady now. All wells are pumping at their safe yields for the following hrs/day, controlled by timers: Well #1 5 hrs/day; Well #3 8 hrs/day; Well #4 14 hrs/day; Well #5 9 hrs/day; Well #6 8 hrs/day; Well #7 (Park Well/emergency well) no longer being used; not needed; Well #8 14 hrs/day. Repairing leaks, but accountability is satisfactory. | 900 |  |
| 1195050 | Town of Appalachia | reservoir | N | W 05/12/08: down 9.5" from overflow. 96 MG left, 212 days ± 10 left. Level was 4" down on 4/14/08. Our concern about this source is low due to their ability, achieved last year, to pump from the Powell River into the reservoir. Not currently pumping from river. | 3,280 |  |
| 2003250 | Albemarle County / Crozet | Beaver Creek Reservoir | V | S - Beaver Creek Reservoir is full. Drought Watch still in effect since 1/2/08 | 5,768 |  |
| 2003600 | Charlottesville/Albemarle County | Sugar Hollow and Ragged Mountain Reservoirs (Observatory WTP) | V | S - Sugar Hollow reservoir is full. Ragged Mountain reservoir is full. Drought Watch still in effect since 1/2/08 | 40,743 |  |
| 2003675 | Albemarle County / Scottsville | Totier Creek Reservoir | V | S - Totier Creek reservoir is full. Drought Watch still in effect since 1/2/08 | 700 |  |
| 2003725 | Charlottesville/Albemarle County | South Fork Rivanna (South Rivanna WTP) | V | S - South Fork Rivanna reservoir is full. Drought Watch still in effect since 1/2/08 | 54,200 |  |
| 2023720 | Town of Troutville | Five Drilled Wells | N | S - Town reported the pumping rate of their No. 3 well dropped from 123 gpm to 40 gpm. The pumping rates of the other four wells are the same. | 500 |  |
| 2023730 | Dal-Nita Hills | Drilled Well | V | B - Well yield has increased from to 4 to 5 gpm to 17 gpm. Owner is hauling water, as needed, to keep storage tank full. Letter provided to the customers advising them of the situation. | 100 |  |
| 2043125 | Berryville, Town of | Shenandoah River | V | S - Voluntary conservation requested on 11 December 2007. | 2,965 |  |
| 2065250 | Fluvanna Correctional Center for Women | Mechunk Creek and on-site Raw Water Reservoir | V | B - Reservoir is 95% full (~38 MG stored). Moderate Drought Condition continues to conserve water. | 1,650 |  |
| 2171750 | Town of Strasburg | North Fork Shenandoah River | V | S - Voluntary conservation has been requested. Stream flow approx 487 cfs on 17 April 2008 | 4,500 |  |
| 2560100 | Town of Clifton Forge | Smith Creek | V | S - Voluntary conservation has been requested. | 4,679 |  |
| 2660345 | City of Harrisonburg | North River, Dry River/Switzer Reservoir (Rawley Springs) | V | S - Voluntary conservation has been requested. This has not been implemented as a result of limited low source water quantity, but rather at the request of the Governor's letter requesting conservation. | 44,500 |  |
| 3053280 | DCWA Central (Dinwiddie County) | Appomattox River Water Authority (ARWA) | N | S - Lifted restrictions on 12/27/07. | 6,800 |  |
| 3081550 | GCWSA - Jarratt | Nottoway River | N | S - Waterworks production rate still reduced due to lower demand; river level and discharge higher than April and sufficient to allow plant operation at 2.0 mgd | 7,190 |  |
| 3093120 | Isle of Wight County | Suffolk | V | B - follows Suffolk's lead on conservation. | 1,284 |  |
| 3149700 | Puddledock Road (Prince George County) | ARWA | N | S - Lifted restrictions on 12/28/07. | 6,525 |  |
| 3550050 | Chesapeake - Western Branch system | City of Portsmouth | V | S -This portion of the city is consecutive to (receives water from) the city of Portsmouth. City Council voted to go to voluntary conservation city-wide - it took effect on 24 Oct 2007. Still following Portsmouth's lead on conservation. | 36,407 |  |
| 3550051 | Chesapeake | Northwest River, City of Norfolk Raw Water (Lake Gaston) | V | S - City Council voted to go to voluntary conservation city-wide - took effect on 24 Oct 2007. Chlorides are used as an indicator of drought, the higher the levels the more concentrated the contaminant in a lesser amount of surface water. The chlorides have been average (40 mg/l) since the recent rains. City is still encouraging voluntary conservation measures. | 101,175 |  |
| 3550052 | Chesapeake - South Norfolk system | City of Norfolk | V | S - 4/17/08-This portion of the city is consecutive to (receives water from) the city of Norfolk. City Council voted to go to voluntary conservation city-wide - it took effect on 24 Oct 2007. Still following Norfolk's lead on conservation. | 38,608 |  |
| 3570150 | Colonial Heights | ARWA | N | S - Lifted restrictions on 12/1/07. | 17,286 |  |
| 3595250 | Emporia | Meherrin River | N | S - Water is going over the dam. | 5,600 |  |
| 3670800 | Virginia-American Water Company (Hopewell) | Appomattox & James Rivers | N | B - Area received high volume of rain in April. Intake levels are at mid-range or higher. The turbidity levels have not gone up considerably, but alkalinity values have decreased significantly. | 25000 - Primary / 42463 Total including Consecutive System (Ft. Lee) |  |
| 3710100 | Norfolk | Lake Prince, Lake Burnt Mills, Western Branch reservoir, Nottoway River, Blackwater River, 4 western wells; Little Creek reservoir, Lakes Smith, Lawson, Whitehurst, and Wright. Lake Gaston. | V | B - As of 05/12, reservoirs at 95.8% (up from 91.0% on 04/14). Historic reservoir capacity is 94.7%. Avg. pumping: Lake Gaston = 6.7 MGD; Blackwater River = 10.8 MGD; Nottoway River = 14.0 MGD; Deep wells = 0 MGD; Spillway elev.: Western Branch -0.1 ft; Lake Prince 0.0 ft; Burnt Mils -3.7 ft; Lake Wright 0.2 ft; Lake Smith 0.3 ft; Blackwater River 10.8 ft; Nottoway River 14.0 ft. Called for voluntary conservation 11/1/07. | 261,250 - Primary / 755,617 - Total including consecutive systems (Va Beach + military bases). |  |
| 3730750 | Petersburg | ARWA | N | S - Lifted restrictions on 1/8/08. | 39,386 |  |
| 3740600 | Portsmouth | Lakes Cohoon, Meade, Kilby, and Speights Run | V | B - As of 05/12, reservoirs at 100% (same as on 04/11). Median reservoir capacity is 100%, average capacity is 98% (period of 1969-2006). Both emergency wells are OFF. Estimated 245 days of reservoir storage remaining at current pumpage and no rainfall. Called for voluntary conservation on 10/10/07. | 100,400 - Primary / 120,400 Total including consecutive systems (military bases) |  |
| 3800805 | Suffolk | Lone Star Lakes, Cumps Mill Pond | V | B - Will follow Portsmouth's lead and the region as far as conservation. As of 5/12/08-Reservoir levels look good. Southern Lakes at 78% capacity, for the Northern Lakes at 100% and Crumps Mill Pond at 86% The Southern Lakes are for emergency use only. Still purchasing water from Portsmouth per their contract, no drought measure taken to date. | 62,562 |  |
| 3810900 | Virginia Beach | Norfolk | V | B - obtains water from Norfolk. Called for voluntary conservation on 9/19/07. | 423,743 |  |
| 4041035 | APPOMATTOX RIVER WATER AUTHORITY | Surface water; Lake Chesdin | N | S- Wholesaler to Chesterfield County, Prince George County, Dinwiddie County; Cities of Petersburg and Colonial Heights. Water level is normal. | 200,000 |  |
| 4041845 | CHESTERFIELD CO CENTRAL WATER SYSTEM | Surface water; Swift Creek reservoir; purchases finished water | N | S- Purchases water from the City of Richmond and the Appomattox River Water Authority. | 263,000 |  |
| 4057800 | TAPPAHANNOCK, TOWN OF | Groundwater wells | N | S- | 2,100 |  |
| 4073311 | GLOUCESTER CO WATER TREATMENT PLT | Surface water, Beaverdam reservoir; 2 deep groundwater wells | N | S-Reservoir at 100%. | 8,870 |  |
| 4075283 | EASTERN GOOCHLAND CENTRAL WATER SYSTEM | Purchased surface water | N | S-purchases water from Henrico County | 2,500 |  |
| 4075735 | JAMES RIVER CORRECTIONAL CTR | Surface water; James River | N | S | 9,300 |  |
| 4085398 | HANOVER SUBURBAN WATER SYSTEM | Surface water; North Anna River; some groundwater wells; purchases finished water | N | S | 71,000 |  |
| 4085770 | SPRING MEADOWS-MEADOW GATE | Groundwater wells | N | S- A replacement well will be drilled shortly and other improvements are proposed in the PER. | 2,300 |  |
| 4087125 | HENRICO COUNTY WATER SYSTEM | Surface water; James River | N | S- Similar to City of Richmond | 289,000 |  |
| 4101900 | WEST POINT, TOWN OF | Groundwater wells | N | S | 3,000 |  |
| 4127110 | DELMARVA PROPERTIES | Groundwater wells | V | S-New Kent Co. encourages conservation at all county owned waterworks. | 7,700 |  |
| 4145675 | POWHATAN COURTHOUSE | Groundwater wells | N | S | 2,600 |  |
| 4193280 | COLONIAL BEACH, TOWN OF | Groundwater wells | N | S | 3,300 |  |
| 4760100 | RICHMOND, CITY OF | Surface water; James River | N | S-water levels in the James River are back to normal; under James River Regional Flow Management Plan; counties of Henrico, Chesterfield, Goochland, and Hanover counties purchase water from the City. | 197,000 |  |
| 5515050 | City of Bedford | Stoney Creek Reservoir and Wells 1 to 5 | N | S - overflowing | 6,946 |  |
| 5143210 | Town of Gretna | Georges Creek Res | N | B - Town is moving forward on new supplemental source development | 2,500 |  |
| 5029085 | Buckingham County | Troublesome Creek Reservoir | N | B | 5,751 |  |
| 5037300 | Town of Keysville | Keysville Reservoir | N | B | 800 |  |
| 5083550 | Town of Halifax | Bannister River Reservoir | N | B | 1,389 |  |
| 5780600 | Town of South Boston | Dan River | N | B | 9,726 |  |
| 5141640 | Town of Stuart | South Mayo River | N | B | 1,500 |  |
| 5147170 | Town of Farmville | Appomattox River | N | B | 7,011 |  |
| 5011050 | Town of Appomattox | Wells | V | B - Operation reports show water levels rising in the wells. The town is actively looking for additional water sources. | 1,708 |  |
| 5135160 | Town of Crewe | Crystal Lake | N | B - overflowing | 3,500 |  |
| 5111450 | Town of Kenbridge | Flat Rock Creek and Offstream Reservoir | N | S - good levels, plenty of rain | 1,400 |  |
| 5067785 | Ridgscrest | Wells | N | B | 52 |  |
| 5067265 | Hales Point | Wells | N | B | 46 |  |
| 5067937 | Stripers Landing | Wells | N | B | 125 |  |
| 5680200 | City of Lynchburg | Pedlar Reservoir | N | B - Overflowing spillway | 76,000 |  |
| 6047070 | Emerald Hill Elementary School | Groundwater | N | S - Well EHS-3 is onstream at a reliable production rate of 12 gpm. Well 1 has been reworked for improved production. Water hauling is no longer needed. | 977 |  |
| 6047500 | Town of Culpeper | Lake Pelham | N | S - On Monday, May 12, 2008, Lake Pelham continued to be full. | 14,200 |  |
| 6061200 | Marshall | Groundwater | M | S - No water was hauled in March. Water ditribution system repairs and line replacements are being done. | 2,134 |  |
| 6061600 | Town of Warrenton | Reservoir on Cedar Run and groundwater | N | S - On Monday, 5/12/08, Warrenton Reservoir is full. Airlie Reservoir is full. | 11,160 |  |
| 6107150 | Town of Hamilton | Groundwater | M | S - 5/12/08 Water levels in wells improving. Several problems with well controls. Town Council voted to maintain Mandatory water use restrictions until new Well 14 is placed in service. | 2,000 |  |
| 6107200 | Town of Hillsboro | Spring/Well | N | B - Increased flow from spring has been adequate to meet current demand. A leak survey revealed 10 potential leaks in the distribution system. | 58 |  |
| 6107221 | LCSA Lenah Farms | Groundwater | V | S - 5/12/08 Voluntary conservation in place beginning 3/11/08. | 810 |  |
| 6107350 | Loudoun County Sanitation Authority | Purchase treated surface water from FCWA (Potomac River) and City of Fairfax (Goose Creek Reservoir) | V | S - 5/12/08 Voluntary conservation in place beginning 3/11/08. | 167,904 |  |
| 6107400 | Town of Lovettsville | Groundwater | V | S - 5/12/08 Voluntary water use restrictions remain in place; however there is no problem with water supply. | 1,280 |  |
| 6107450 | Town of Middleburg | Groundwater | V | B - 5/12/08 - Voluntary water use restrictions replace mandatory water use restrictions on 4/10/08. | 590 |  |
| 6107600 | Town of Purcellville | Hirst Reservoir and groundwater | V | B -- 5/12/08 Reservoir is full. Mandatory water conservation replaced with voluntary water conservation, 4/2/08. | 6,300 |  |
| 6107650 | Town of Round Hill | Groundwater | V | B - 5/12/08 - Voluntary water use restrictions replace mandatory water use restrictions on 4/1/08. | 3,156 |  |
| 6113200 | Town of Madison | White Oak Run | N | S -- Stream flow remains adequate to meet normal demands. | 778 |  |
| 6137300 | Rapidan Service Authority - Rt. 15 | Purchase treated surface water from Town of Orange (Rapidan River) | N | S - Town of Orange raw water availability is well above minimum. | 273 |  |
| 6137400 | Town of Gordonsville | Purchase treated surface water from RSA and Town of Orange | N | S--No water use restrictions are in place. | 1,800 |  |
| 6137500 | Town of Orange | Rapidan River | V | S - 5/12/08 - Fourteen day running average of Rapidan River flow is 1663 cfs (withdrawal restrictions are imposed below 44 cfs). | 4,500 |  |
| 6137999 | Rapidan Service Authority - Wilderness and Lake of the Woods | Rapidan River | N | Rapidan River flow has been steady at an adequate level. | 11,331 |  |
| 6153260 | Woodbridge Mobile Home Park | Groundwater | M | S -- 5/12/08 Waterworks continues to have episodes of low pressure due to inadequate sources and leaks in the distribution system. This problem is indirectly related to drought as source problems existed previously. | 320 |  |
| 6600100 | City of Fairfax | Goose Creek Reservoir | N | B -- 5/12/08 - Beaver Dam Reservoir is full. Lifted voluntary water use restrictions on 4/7/08. | 45,000 |  |
| 6179100 and 6179775 | Stafford County | Smith Lake and Abel Lake | V | B -- Both lakes are still full. Mandatory restrictions went into effect 9/17/07, were increased 10/8/07, and were reduced 2/19/08. Mandatory restrictions lifted 3/18/08. | 53,086 |  |
| Notes of interest: |  |  |  |  |  |
| (1) Metropolitan Washington Council of Governments lifted the drought Watch, returning to Normal status, lifting a region-wide voluntary conservation advisory, on 4/1/08, covering DC, Maryland, and Northern Virginia. |  |
| (2) Interstate Commission on the Potomac River Basin (ICPRB) gathers meterological, drought, and water supply data from all of the major water suppliers in the Metro Washington area and determines the need for upstream reservoir releases, if any, to augment the flow in the Potomac River for water supply withdrawal. ICPRB has predicted that likelihood of releases from upstream reservoirs is slightly below normal. |  |

APPENDIX F

APPENDIX G

Drought Watch -- USGS State Information on Drought

Map of below normal 7-day average streamflow

APPENDIX H

Virginia Climate Response Network

May 16, 2008